## Slide 1: Lecture 6 – Memory Access Performance
Lecture 6.1 - DRAM Bandwidth
CSD2170 Programming Massively Parallel Processors

## Slide 2: Objective
To learn that memory bandwidth is a first-order performance factor in a massively parallel processor
  DRAM bursts, banks, and channels
  All concepts are also applicable to modern multicore processors

## Slide 3: Global Memory (DRAM) Bandwidth
Ideal
Reality

## Slide 4: DRAM Core Array Organization
Each DRAM core array has about 16M bits
Each bit is stored in a tiny capacitor made of one transistor
Memory Cell
Core Array
Row
Decoder
Sense Amps
Column Latches
Mux
Row
Addr
Column
Addr
Off-chip Data
Wide
Narrow
Pin Interface

## Slide 5: A very small (8x2-bit) DRAM Core Array
decode
0
1
1
Sense amps
Mux

## Slide 6: DRAM Core Arrays are Slow
Reading from a cell in the core array is a very slow process
  DDR: Core speed = ½ interface speed
  DDR2/GDDR3: Core speed = ¼ interface speed
  DDR3/GDDR4: Core speed = ⅛ interface speed
  … likely to be worse in the future
decode
To sense amps
A very small capacitance that stores a data bit
About 1000 cells connected to each vertical line

## Slide 7: DRAM Bursting
For DDR{2,3} SDRAM cores clocked at 1/N speed of the interface:
  Load (N × interface width) of DRAM bits from the same row at once to an internal buffer, then transfer in N steps at interface speed
  DDR3/GDDR4: buffer width = 8X interface width

## Slide 8: DRAM Bursting Timing Example
time
Address bits to decoder
Core Array access delay
bits
on interface
Non-burst timing
Burst timing
Modern DRAM systems are designed to always be accessed in burst mode. Burst bytes are transferred to the processor but discarded when accesses are not to sequential locations.

## Slide 9: Multiple DRAM Banks
decode
Sense amps
Mux
decode
Sense amps
Mux
Bank 0
Bank 1

## Slide 10: DRAM Bursting with Banking
Single-Bank burst timing, dead time on interface
Multi-Bank burst timing, reduced dead time

## Slide 11: GPU off-chip memory subsystem
NVIDIA GTX280 GPU:
  Peak global memory bandwidth = 141.7GB/s
Global memory (GDDR3) interface @ 1.1GHz
  (Core speed @ 276Mhz)
  For a typical 64-bit interface, we can sustain only about 17.6 GB/s (Recall DDR - 2 transfers per clock)
  We need a lot more bandwidth (141.7 GB/s) – thus 8 memory channels

## Slide 12: Lecture 6 – Memory Access Performance
Lecture 6.1 - Memory Coalescing in CUDA
CSD2170 Programming Massively Parallel Processors

## Slide 13: Objective
To learn that memory coalescing is important for effectively utilizing memory bandwidth in CUDA
  Its origin in DRAM burst
  Checking if a CUDA memory access is coalesced
  Techniques for improving memory coalescing in CUDA code

## Slide 14: DRAM Burst – A System View
Each address space is partitioned into burst sections
  Whenever a location is accessed, all other locations in the same section are also delivered to the processor
Basic example: a 16-byte address space, 4-byte burst sections
  In practice, we have at least 4GB address space, burst section sizes of 128-bytes or more
2
1
0
3
5
4
6
7
9
8
10
11
13
12
14
15
Burst section
Burst section
Burst section
Burst section

## Slide 15: Memory Coalescing
When all threads of a warp execute a load instruction, if all accessed locations fall into the same burst section, only one DRAM request will be made and the access is fully coalesced.
2
1
0
3
5
4
6
7
9
8
10
11
13
12
14
15
Burst section
Burst section
Burst section
Burst section
T0
T1
T2
T3
Coalesced Loads
T0
T1
T2
T3
Coalesced Loads

## Slide 16: Un-coalesced Accesses
When the accessed locations spread across burst section boundaries:
  Coalescing fails
  Multiple DRAM requests are made
  The access is not fully coalesced.
Some of the bytes accessed and transferred are not used by the threads
2
1
0
3
5
4
6
7
9
8
10
11
13
12
14
15
Burst section
Burst section
Burst section
Burst section
T0
T1
T2
T3
Un-coalesced Loads
T0
T1
T2
T3
Un-coalesced Loads

## Slide 17: How to judge if an access is coalesced?
Accesses in a warp are to consecutive locations if the index in an array access is in the form of
  A[(expression with terms independent of threadIdx.x) + threadIdx.x];

## Slide 18: A 2D C Array in Linear Memory Space
M0,2
M1,1
M0,1
M0,0
M1,0
M0,3
M1,2
M1,3
M0,2
M0,1
M0,0
M0,3
M1,1
M1,0
M1,2
M1,3
M2,1
M2,0
M2,2
M2,3
M2,1
M2,0
M2,2
M2,3
M3,1
M3,0
M3,2
M3,3
M3,1
M3,0
M3,2
M3,3
M
linearized order in increasing address

## Slide 19: Two Access Patterns of Basic Matrix Multiplication
A
B
WIDTH
Thread 1
Thread 2
A[Row*n+i]
B[i*k+Col]
i is the loop counter in the inner product loop of the kernel code
A is m n, B is n k
Col = blockIdx.x*blockDim.x + threadIdx.x
HEIGHT

## Slide 20: B accesses are coalesced
N
T0
T1
T2
T3
Load iteration 0
T0
T1
T2
T3
Load iteration 1
Access direction in kernel code
B0,2
B1,1
B0,1
B0,0
B1,0
B0,3
B1,2
B1,3
B2,1
B2,0
B2,2
B2,3
B3,1
B3,0
B3,2
B3,3
B0,2
B0,1
B0,0
B0,3
B1,1
B1,0
B1,2
B1,3
B2,1
B2,0
B2,2
B2,3
B3,1
B3,0
B3,2
B3,3

## Slide 21: A Accesses are Not Coalesced
T0
T1
T2
T3
Load iteration 0
T0
T1
T2
T3
Load iteration 1
Access direction in kernel code
…
A0,2
A1,1
A0,1
A0,0
A1,0
A0,3
A1,2
A1,3
A2,1
A2,0
A2,2
A2,3
A3,1
A3,0
A3,2
A3,3
A0,2
A0,1
A0,0
A0,3
A1,1
A1,0
A1,2
A1,3
A2,1
A2,0
A2,2
A2,3
A3,1
A3,0
A3,2
A3,3

## Slide 22: Loading an Input Tile
A
B
C
WIDTH
Row
Col
n
m
n
k
k
m
int tx = threadIdx.x
int ty = threadIdx.y
Accessing tile 0 2D indexing:
A[Row][tx]
B[ty][Col]
Have each thread load an A element
and a B element at the same relative
position as its C element.
Notes: Point out that I and j will become global thread indices.

## Slide 23: Corner Turning
d_M
d_N
W
I
D
T
H
WIDTH
d_M
d_N
Original
Access
Pattern
Tiled
Access
Pattern
Copy into
shared
memory
Perform
multiplication
with shared memory
values