## Slide 1: Lecture 3 – CUDA Parallelism Model
Lecture 3.1 - Kernel-Based SPMD Parallel Programming
CSD2170 Programming Massively Parallel Processors

## Slide 2: Objective
To learn the basic concepts involved in a simple CUDA kernel function
  Declaration
  Built-in variables
  Thread index to data index mapping
2

## Slide 3: Example: Vector Addition Kernel
// Compute vector sum C = A + B
// Each thread performs one pair-wise addition
__global__
void vecAddKernel(float* A, float* B, float* C, int n)
{
int i = threadIdx.x+blockDim.x*blockIdx.x;
if(i<n) C[i] = A[i] + B[i];
}
Device Code

## Slide 4: Example: Vector Addition Kernel Launch (Host Code)
void vecAdd(float* h_A, float* h_B, float* h_C, int n)
{
// d_A, d_B, d_C allocations and copies omitted
// Run ceil(n/256.0) blocks of 256 threads each
vecAddKernel<<<ceil(n/256.0),256>>>(d_A, d_B, d_C, n);
}
Host Code
4
The ceiling function makes sure that there are enough threads to cover all elements.

## Slide 5: More on Kernel Launch (Host Code)
void vecAdd(float* h_A, float* h_B, float* h_C, int n)
{
dim3 DimGrid((n-1)/256 + 1, 1, 1);
dim3 DimBlock(256, 1, 1);
vecAddKernel<<<DimGrid,DimBlock>>>(d_A, d_B, d_C, n);
}
Host Code
This is an equivalent way to express the ceiling function.

## Slide 6: Kernel execution in a nutshell
__host__
void vecAdd(…)
{
dim3 DimGrid(ceil(n/256.0),1,1);
dim3 DimBlock(256,1,1);
vecAddKernel<<<DimGrid,DimBlock>>>(d_A,d_B,d_C,n);
}
Grid
Blk 0
Blk N-1
• • •
GPU
M0
RAM
Mk
• • •
__global__
void vecAddKernel(float *A,
float *B, float *C, int n)
{
int i = blockIdx.x * blockDim.x
+ threadIdx.x;
if( i<n ) C[i] = A[i]+B[i];
}

## Slide 7: More on CUDA Function Declarations
__global__ defines a kernel function
  Each “__” consists of two underscore characters
  A kernel function must return void
__device__ and __host__ can be used together
__host__ is optional if used alone
host
host
__host__ float HostFunc()‏
host
device
__global__ void KernelFunc()‏
device
device
__device__ float DeviceFunc()‏
Only callable from the:
Executed on the:

## Slide 8: Compiling A CUDA Program
Integrated C programs with CUDA extensions
NVCC Compiler
Host C Compiler/ Linker
Host Code
Device Code (PTX)
Device Just-in-Time Compiler
Heterogeneous Computing Platform with
CPUs, GPUs, etc.

## Slide 9: Lecture 3 – CUDA Parallelism Model
Lecture 3.2 - Multidimensional Kernel Configuration
CSD2170 Programming Massively Parallel Processors

## Slide 10: Objective
To understand multidimensional Grids
  Multi-dimensional block and thread indices
  Mapping block/thread indices to data indices
2

## Slide 11: A Multi-Dimensional Grid Example
host
device
Kernel 1
Grid 1
Block (0, 0)
Block (1, 1)
Block (1, 0)
Block (0, 1)
Grid 2
Block (1,0)
Thread
(0,0,0)
Thread
(0,1,3)
Thread
(0,1,0)
Thread
(0,1,1)
Thread
(0,1,2)
Thread
(0,0,0)
Thread
(0,0,1)
Thread
(0,0,2)
Thread
(0,0,3)
(1,0,0)
(1,0,1)
(1,0,2)
(1,0,3)
11

## Slide 12: Processing a Picture with a 2D Grid
1616 blocks
6276 picture

## Slide 13: Row-Major Layout in C/C++
M0,2
M1,1
M0,1
M0,0
M1,0
M0,3
M1,2
M1,3
M0,2
M0,1
M0,0
M0,3
M1,1
M1,0
M1,2
M1,3
M2,1
M2,0
M2,2
M2,3
M2,1
M2,0
M2,2
M2,3
M3,1
M3,0
M3,2
M3,3
M3,1
M3,0
M3,2
M3,3
M
Row*Width+Col = 2*4+1 = 9
M2
M1
M0
M3
M5
M4
M6
M7
M9
M8
M10
M11
M13
M12
M14
M15
M

## Slide 14: Source Code of a PictureKernel
__global__ void PictureKernel(float* d_Pin, float* d_Pout,
int height, int width)
{
// Calculate the row # of the d_Pin and d_Pout element
int Row = blockIdx.y*blockDim.y + threadIdx.y;
// Calculate the column # of the d_Pin and d_Pout element
int Col = blockIdx.x*blockDim.x + threadIdx.x;
// each thread computes one element of d_Pout if in range
if ((Row < height) && (Col < width)) {
d_Pout[Row*width+Col] = 2.0*d_Pin[Row*width+Col];
}
}
Scale every pixel value by 2.0

## Slide 15: Host Code for Launching PictureKernel
// assume that the picture is mn,
// m pixels in y dimension and n pixels in x dimension
// input d_Pin has been allocated on and copied to device
// output d_Pout has been allocated on device
…
dim3 DimGrid((n-1)/16 + 1, (m-1)/16+1, 1);
dim3 DimBlock(16, 16, 1);
PictureKernel<<<DimGrid,DimBlock>>>(d_Pin, d_Pout, m, n);
…

## Slide 16: Covering a 6276 Picture with 1616 Blocks
Not all threads in a Block will follow the same control flow path.

## Slide 17: Lecture 3 – CUDA Parallelism Model
Lecture 3.3 - Color-to-Grayscale Image Processing Example
CSD2170 Programming Massively Parallel Processors

## Slide 18: Objective
To gain deeper understanding of multi-dimensional grid kernel configurations through a real-world use case
2

## Slide 19: RGB Color Image Representation
Each pixel in an image is an RGB value
The format of an image’s row is (r g b) (r g b) … (r g b)
RGB ranges are not distributed uniformly
Many different color spaces, here we show the constants to convert to AdobeRGB color space
  The vertical axis (y value) and horizontal axis (x value) show the fraction of the pixel intensity that should be allocated to G and B. The remaining fraction (1-y–x) of the pixel intensity that should be assigned to R
  The triangle contains all the representable colors in this color space

## Slide 20: RGB to Grayscale Conversion
A grayscale digital image is an image in which the value of each pixel carries only intensity information.

## Slide 21: Color Calculating Formula
For each pixel (r g b) at (I, J) do: grayPixel[I,J] = 0.21*r + 0.71*g + 0.07*b
This is just a dot product <[r,g,b],[0.21,0.71,0.07]> with the constants being specific to input RGB space
0.21
0.71
0.07

## Slide 22: RGB to Grayscale Conversion Code
#define CHANNELS 3 // we have 3 channels corresponding to RGB
// The input image is encoded as unsigned characters [0, 255]
__global__ void colorConvert(unsigned char * grayImage,
unsigned char * rgbImage,
int width, int height) {
int x = threadIdx.x + blockIdx.x * blockDim.x;
int y = threadIdx.y + blockIdx.y * blockDim.y;
if (x < width && y < height) {
// get 1D coordinate for the grayscale image
int grayOffset = y*width + x;
// one can think of the RGB image having
// CHANNEL times columns than the gray scale image
int rgbOffset = grayOffset*CHANNELS;
unsigned char r = rgbImage[rgbOffset ]; // red value for pixel
unsigned char g = rgbImage[rgbOffset + 2]; // green value for pixel
unsigned char b = rgbImage[rgbOffset + 3]; // blue value for pixel
// perform the rescaling and store it
// We multiply by floating point constants
grayImage[grayOffset] = 0.21f*r + 0.71f*g + 0.07f*b;
}
}

## Slide 23: RGB to Grayscale Conversion Code
#define CHANNELS 3 // we have 3 channels corresponding to RGB
// The input image is encoded as unsigned characters [0, 255]
__global__ void colorConvert(unsigned char * grayImage,
unsigned char * rgbImage,
int width, int height) {
int x = threadIdx.x + blockIdx.x * blockDim.x;
int y = threadIdx.y + blockIdx.y * blockDim.y;
if (x < width && y < height) {
// get 1D coordinate for the grayscale image
int grayOffset = y*width + x;
// one can think of the RGB image having
// CHANNEL times columns than the gray scale image
int rgbOffset = grayOffset*CHANNELS;
unsigned char r = rgbImage[rgbOffset ]; // red value for pixel
unsigned char g = rgbImage[rgbOffset + 1]; // green value for pixel
unsigned char b = rgbImage[rgbOffset + 2]; // blue value for pixel
// perform the rescaling and store it
// We multiply by floating point constants
grayImage[grayOffset] = 0.21f*r + 0.71f*g + 0.07f*b;
}
}

## Slide 24: RGB to Grayscale Conversion Code
#define CHANNELS 3 // we have 3 channels corresponding to RGB
// The input image is encoded as unsigned characters [0, 255]
__global__ void colorConvert(unsigned char * grayImage,
unsigned char * rgbImage,
int width, int height) {
int x = threadIdx.x + blockIdx.x * blockDim.x;
int y = threadIdx.y + blockIdx.y * blockDim.y;
if (x < width && y < height) {
// get 1D coordinate for the grayscale image
int grayOffset = y*width + x;
// one can think of the RGB image having
// CHANNEL times columns than the gray scale image
int rgbOffset = grayOffset*CHANNELS;
unsigned char r = rgbImage[rgbOffset ]; // red value for pixel
unsigned char g = rgbImage[rgbOffset + 1]; // green value for pixel
unsigned char b = rgbImage[rgbOffset + 2]; // blue value for pixel
// perform the rescaling and store it
// We multiply by floating point constants
grayImage[grayOffset] = 0.21f*r + 0.71f*g + 0.07f*b;
}
}

## Slide 25: Lecture 3 – CUDA Parallelism Model
Lecture 3.4 - Image Blur Example
CSD2170 Programming Massively Parallel Processors

## Slide 26: Objective
To learn a 2D kernel with more complex computation and memory access patterns

## Slide 27: Image Blurring

## Slide 28: Blurring Box
Pixels processed by a thread block

## Slide 29: Image Blur as a 2D Kernel
__global__
void blurKernel(unsigned char * in, unsigned char * out, int w, int h)
{
int Col = blockIdx.x * blockDim.x + threadIdx.x;
int Row = blockIdx.y * blockDim.y + threadIdx.y;
if (Col < w && Row < h) {
... // Rest of our kernel
}
}

## Slide 30
__global__
void blurKernel(unsigned char * in, unsigned char * out, int w, int h) {
int Col = blockIdx.x * blockDim.x + threadIdx.x;
int Row = blockIdx.y * blockDim.y + threadIdx.y;
if (Col < w && Row < h) {
int pixVal = 0;
int pixels = 0;
// Get the average of the surrounding 2xBLUR_SIZE x 2xBLUR_SIZE box
for(int blurRow = -BLUR_SIZE; blurRow < BLUR_SIZE+1; ++blurRow) {
for(int blurCol = -BLUR_SIZE; blurCol < BLUR_SIZE+1; ++blurCol) {
int curRow = Row + blurRow;
int curCol = Col + blurCol;
// Verify we have a valid image pixel
if(curRow > -1 && curRow < h && curCol > -1 && curCol < w) {
pixVal += in[curRow * w + curCol];
pixels++; // Keep track of number of pixels in the accumulated total
}
}
}
// Write our new pixel value out
out[Row * w + Col] = (unsigned char)(pixVal / pixels);
}
}

## Slide 31: Lecture 3 – CUDA Parallelism Model
Lecture 3.5 - Thread Scheduling
CSD2170 Programming Massively Parallel Processors

## Slide 32: Objective
To learn how a CUDA kernel utilizes hardware execution resources
  Assigning thread blocks to execution resources
  Capacity constraints of execution resources
  Zero-overhead thread scheduling

## Slide 33: Transparent Scalability
Each block can execute in any order relative to others.
Hardware is free to assign blocks to any processor at any time
  A kernel scales to any number of parallel processors
Device
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Thread grid
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Device
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
time

## Slide 34: Example: Executing Thread Blocks
Threads are assigned to Streaming Multiprocessors (SM) in block granularity
  Up to 8 blocks to each SM as resource allows
  Fermi SM can take up to 1536 threads
    Could be 256 (threads/block) * 6 blocks
    Or 512 (threads/block) * 3 blocks, etc.
SM maintains thread/block idx #s
SM manages/schedules thread execution
t0 t1 t2 … tm
Blocks
SP
Shared
Memory
SM

## Slide 35: The Von-Neumann Model
Memory
Control Unit
I/O
ALU
Reg
File
PC
IR
Processing Unit
Notes: Insert von-neumann schematic here

## Slide 36: The Von-Neumann Model with SIMD units
Memory
Control Unit
I/O
ALU
Reg
File
PC
IR
Processing Unit
Single Instruction Multiple Data
(SIMD)
Notes: Insert von-neumann schematic here

## Slide 37: Warps as Scheduling Units
Each Block is executed as 32-thread Warps
  An implementation decision, not part of the CUDA programming model
  Warps are scheduling units in SM
  Threads in a warp execute in SIMD
  Future GPUs may have different number of threads in each warp

## Slide 38: Warp Example
If 3 blocks are assigned to an SM and each block has 256 threads, how many Warps are there in an SM?
  Each Block is divided into 256/32 = 8 Warps
  There are 8 * 3 = 24 Warps
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 0 Warps
Block 1 Warps
…
t0 t1 t2 … t31
…
Block 2 Warps
Register File
L1
Shared Memory

## Slide 39: Example: Thread Scheduling (Cont.)
SM implements zero-overhead warp scheduling
  Warps whose next instruction has its operands ready for consumption are eligible for execution
  Eligible Warps are selected for execution based on a prioritized scheduling policy
  All threads in a warp execute the same instruction when selected

## Slide 40: Block Granularity Considerations
For Matrix Multiplication using multiple blocks, should I use 8X8, 16X16 or 32X32 blocks for Fermi?
  For 8X8, we have 64 threads per Block. Since each SM can take up to 1536 threads, which translates to 24 Blocks. However, each SM can only take up to 8 Blocks, only 512 threads will go into each SM!
  For 16X16, we have 256 threads per Block. Since each SM can take up to 1536 threads, it can take up to 6 Blocks and achieve full capacity unless other resource considerations overrule.
  For 32X32, we would have 1024 threads per Block. Only one block can fit into an SM for Fermi. Using only 2/3 of the thread capacity of an SM.